## Slide 1: Descriptive and inferential statistical methodologies have proven effective in creating a proactive ‘alarm’, accurately identifying Pump Failures with Horse Power (HP) and Pump Efficiency (PE) emerging as key variables of interest with deviations of 15 HP and > 3 % PE being our core signal thresholds.
The first slide we want to show is our overall conclusion showcasing that we have been able to effectively create a multivariate regressive equation that models Pump Failure.
On this slide, we would like you to show two charts: A) Using a line-series chart, show the Multivariate Regression Equation Values you’ve developed versus the Pump Failure (1 or 0)
B) Using a Column Chart, show the correlations ranked from highest-to-lowest for the Rolling Standard Deviation Dataset
Hint: The Chart you’ve created for the Inferential Statistics Tab, Q8 may be helpful.
You’ve created the chart for B) in Q6 so feel free to re-use this.
We’ve included an example on the right for the line chart and what it may look like.
Note: We’ve included a sample headline for you – you can feel free to use this or modify this as you see fit
Chart: Statistical Alarm Plot

## Slide 2: Descriptive Analysis has enabled us to clearly identify particular signature abnormalities showing clear signature changes in both Rolling Standard Deviation and Rolling Mean Datasets when observed over the respective failure period of interest.
We will transition from Descriptive Statistics through to Inferential.
A) Rolling Standard Deviation Plot
B) Rolling Mean Plot

## Slide 3: Further segmentation of the data via binary means (Pump Failure = 0 or 1) illustrated through <what plots have we used?>, show a clear signature difference between that of normal behaviour and that of Failure with Pump Torque , Pump Efficiency, Pump Torque showing the 3 largest variances.
The third slide will illustrate how we have made use of descriptive statistics plot to identify which variables have exhibited the largest overall variances.
On this slide, we would like you to show four charts: A) Rolling Standard Deviation Plot (Pump Failure = 1), B) Rolling Standard Deviation Plot (Pump Failure = 0), C) Rolling Mean Plot (Pump Failure = 1), D) Rolling Mean Plot (Pump Failure = 0)

## Slide 4: Correlation analyses across datasets yield particularly interesting insights with horse power and pump speed negatively correlated with Pump Failure in the Rolling Standard Deviation Data, whilst horse power and pump speed show a subsequently strong positive correlation in the Rolling Stdev Dataset.
The fourth slide will illustrate how we have made use of inferential statistics to identify which variables have exhibited the largest correlation spreads.
On this slide, we would like you to show three charts.
A) Raw Dataset Correlation against Pump Failure
B) Rolling Mean Dataset Correlation against Pump Failure
C) Rolling Standard Deviation Dataset Correlation against Pump Failure

## Slide 5: Lastly, analysis of the statistical significance of variables contributing towards Pump Failure reveal that with a R Squared of ____, a linear model is a <good/bad> fit for the data with both Rolling Mean and Rolling Standard Deviation datasets contributing key information to understand Pump Failure mechanics.
Variable | P-Value Significance
Volumetric Flow Meter 1 | 0.07776923
Volumetric Flow Meter 2 | 5.141E-11
Pump Speed (RPM) | 0
Pump Torque | 0
Ambient Temperature | 0
Horse Power | 1.99E-216
The fifth and final slide will close out our story and showcase how we have identified which variables are most statistically significant to our Multivariate Linear Regression Model alongside a table showcasing the associated P-Values for these variables.